## Slide 1
Biomechanical female pelvic floor model
H. Čechová & al.
September 2024

## Slide 2
INTRODUCTION
Motivation
  Injury of pelvic floor soft tissues and perineum during vaginal delivery
  Pelvic floor dysfunction (urinary incontinence, fecal incontinence, prolapse) with short-term, long-term or life-long consequences
  Cooperation with medical teams
    Hospital and Medical Faculty of Charles University in Pilsen
    Institute for Mother and Child Care in Prague
    Hospital Frýdek-Místek
Goals
  Personalized female pelvic model, modular approach
  Tool for injury prediction during vaginal delivery
  Pelvic organ prolapse quantification
  Detection of pelvic floor muscles contraction

## Slide 3
PREVIOUSLY DEVELOPED MODELS
2020 birth model
2012 model for manual perineal protection
2017 Study on levator ani muscle

## Slide 4
GEOMETRY
Based on MRI data, slice thickness = 2 mm
Nulliparous woman, 23 years, BMI = 23.15 kg/m2
MRI data segmentation (Slicer 3D)
Surface adjustment and geometry discretisation (Hypermesh, VPS)

## Slide 5
GEOMETRY
Organs covered by endopelvic fascia
Pelvic floor structures

## Slide 6
MODEL GEOMETRY
Pelvic floor structures
Coccygeus + sacrospinal ligament
Obturator internus
Arcus tendinous levatoris ani
Iliococcygeus + puborectalis + pubovisceralis
Anal sphincter
Organs covered by endopelvic fascia
Perineal structures
Perineal body
Perineal membrane
Transversus superficialis
Bulbospongiosus
Ischiocavernosus

## Slide 7
FE MODEL
Pelvis – shell triangular elements
Soft tissues and muscles – solid tetrahedral elements
Perineal membrane – membrane triangular elements
Muscles and ligaments: passive hyperelastic material
Rigid bones
Include contacts

## Slide 8
FE MODEL
Material models
  Pelvis – rigid body
  Muscles – hyperelastic material (Ogden) with parameters obtained from measurements of porcine samples (Havelkova 2019)
  Ligaments - hyperelastic material (Ogden) (Brandao 2015)
  Perineal membrane – linear elastic membrane with two layers of fibers (Cosson 2013)
Tissues coupling
  Contacts
  Tieds
  Boundary conditions (fixed pelvis)
Havelková L, Krofta L, Kochová P, Liška V, Kališ V, Feyereisl J. Persistent occiput posterior position and stress distribution in levator ani muscle during vaginal delivery computed by a finite element model. Int Urogynecol J. 2020;31(7):1315-1324. doi:10.1007/s00192-019-03997-8
Brandão S, Parente M, Mascarenhas T, Da Silva ARG, Ramos I, Jorge RN. Biomechanical study on the bladder neck and urethral positions: Simulation of impairment of the pelvic ligaments. Journal of Biomechanics. 2015;48(2):217-223. doi:10.1016/j.jbiomech.2014.11.045
Cosson M, Rubod C, Vallet A, Witz JF, Dubois P, Brieu M. Simulation of normal pelvic mobilities in building an MRI-validated biomechanical model. Int Urogynecol J. 2013;24(1):105-112. doi:10.1007/s00192-012-1842-8

## Slide 9
Left occiput anterior position of the fetal head
Carus curve based on pelvic anthropometric points (Chen 2023)
Cardinal movements of the fetal head (flexion, internal rotation)
Head diameters: suboccipitobregmatic (SOB), mentovertical (MV), biparietal (BP)
Pelvic planes: pelvic inlet, greatest pelvic cavity, least pelvic cavity (obstetrical outlet), (anatomical) pelvic outlet
SOB is perpendicular to the pelvic planes
PARAMETRIZED HEAD TRAJECTORY
Chen S, Routzong MR, Abramowitch SD, Grimm MJ. A Computational Procedure to Derive the Curve of Carus for Childbirth Computational Modeling. Journal of Biomechanical Engineering. 2023;145(1):011002. doi:10.1115/1.4055108

## Slide 10
PARAMETRIZED HEAD TRAJECTORY
Complex prescription of head rotation in 3D
Trajectory implemented in Matlab

## Slide 11
DELIVERY SIMULATION
Coupling of VPS and SfePy
Delivery simulated in VPS
Sphere with diameter 9.6 cm, follows the Carus curve
Muscles at deformed state exported to SfePy
Computed strain of muscle fibers
Bulbospongiousus extracted

## Slide 12
THANK YOU FOR YOUR ATTENTION
Ing. Hana Čechová, Ph.D.
e-mail: hcechov@ntc.zcu.cz
University of West Bohemia in Pilsen
New Technologies – Research Center
Univerzitní 8, 306 14 Plzeň
URL: http://ntc.zcu.cz
This work was supported by the project no. BYCZ01-014 “Pelvic floor disorder prevention” realised within the frame of the Program INTERREG Bavaria – Czechia 2021–2027. The realisation is supported by financial means of the European Regional Development Fund (80% of the costs) and the state budget of the Czech Republic (10%).